## Slide 1: IPsec Update
Boris Pismenny
November 2017

## Slide 2: Overview
ESN
Trailer removal
VLAN support
Performance Update
Full offload
Notes: IPsec basics
Status
Kernel
  Control path
  Driver’s data path
Linux Near Future
  ESN
  Trailer removal
Performance
DPDK
  Control-path
  Data-path
Full offload

## Slide 3: A Problem with Sequence numbers
With high connection speed sequence numbers are depleted quickly.
For example: Using minimum ESP IPv4 transport mode packets:
Eth + IP + ESP + TCP = 14 + 20 + (16+20) + 20 = 90
Lets calculate how many packets we can pass per second
In the worst case, we can pass packets per second, and the SA needs to be replaced at least every seconds which are 2 minutes.

## Slide 4: Extended Sequence Numbers
From RFC4303 (ESP):
“to support high-speed IPsec implementations, Extended Sequence Numbers (ESNs) SHOULD be implemented, as an extension to the current, 32-bit sequence number field… Only the low-order 32 bits of the sequence number are transmitted in the plaintext ESP header of each packet, thus minimizing packet overhead. The high-order 32 bits are maintained as part of the sequence number counter by both transmitter and receiver and are included in the computation of the ICV in an algorithm/mode-specific fashion.

## Slide 5: ESN
ESN reduces the number of key renegotiation required for high performance tunnels
Send-side ESN:
Provided in the packet IV field
  IV is transformed by hardware to wire format (seqiv – same as Linux)
Receive-side ESN:
Needs state in HW
  HW doesn’t update ESN without software intervention
Periodically updated from software (once every 2^31 packets)
ESN 1 ESN 2 ESN 3
|-------------*-------------|-------------*-------------|-------------*-------------|
^ ^ ^ ^ ^ ^ ^
^ - marks where to call HW to update the ESN state machine.
| - marks the start of the ESN scope (0-2^32-1). When the bottom of the replay window crosses this point move overlap to zero and increment ESN.
* - marks the middle of the ESN scope (2^31). When the bottom of the replay window crosses this point move overlap to one.
SPI
SEQ
IV (ESN)
Send-side ESP header

## Slide 6: Rx trailer removal
Rx trailer removal improves performance by 10%
  From 23.6Gbps to 25.5Gbps on iperf
  No need to access the end of the packet -> Save 1-2 cache line accesses per packet
Next-header field is placed in xfrm_offload(skb)
Tcpdump will never see trailer

## Slide 7: Encapsulations inside encapsulations
In virtualized environments ESP is overlayed with VXLAN/GRE/etc.
  i.e. [VXLAN | ESP | TCP] or [GRE | ESP | TCP]
We suggest to advertise support for crypto offload on the overlay device
  xdo_dev_state_add/del called from the upper device until the physical device.

## Slide 8: Performance – single stream
Chart: 1 unidirectional TCP Stream(s) IPSec tunnel aes256 (40GbE, linked-list)
| TX | RX | TX | RX | TX | RX | TX | RX | TX | RX | 64 | 256 | 1024 | 1500 | 16384
No-IPSec CPU | 16.99 | 1.83 | 16.89 | 3.24 | 16.91 | 8.49 | 16.96 | 11.23 | 7.13 | 14.21
Innova CPU | 17.08 | 2.23 | 17.14 | 3.46 | 17.08 | 10.38 | 13.64 | 26.94 | 4.95 | 26.89
AES-NI CPU | 17.25 | 2.9 | 17.18 | 3.39 | 17.17 | 3.33 | 17.14 | 3.36 | 17.12 | 3.07
No-IPSec | #N/A | 1.8 | #N/A | #N/A | 6.65 | #N/A | #N/A | 22.83 | #N/A | #N/A | 29.72 | #N/A | #N/A | 37.66 | #N/A
Innova | #N/A | 1.52 | #N/A | #N/A | 5.58 | #N/A | #N/A | 19.73 | #N/A | #N/A | 25.39 | #N/A | #N/A | 25.38 | #N/A
AES-NI | #N/A | 1.08 | #N/A | #N/A | 1.83 | #N/A | #N/A | 2.28 | #N/A | #N/A | 2.35 | #N/A | #N/A | 2.77 | #N/A

## Slide 9: IPsec full offload
Full offload will be supported in Connectx6-Lx
Requirements to move from partial offload to full offload:
ESP Decapsulation/Encapsulation
Replay protection
IPsec Policy
Benefits of full offload:
SRIOV – Hypervisor can configure IPsec for all guests. Guests are unaware of IPsec.
RSS according to inner fields
LRO
ESP encapsulation with any other supported encapsulation offload

## Slide 10: IPsec full offload – control path
Driver is called anytime a Security Association or Security Policy is added/deleted.
  Do we need anything else?

## Slide 11: IPsec full offload – data path exceptions
HW will pass IP fragmented packets to the hypervisor without processing
  Software needs an interface to get/set HW replay-protection
  Another option is to drop IP fragments
Hypervisor will forward packets to guest after handling the exception
  Similar to OVS offload slow-path

## Slide 12
Thank You