## Slide 1
Interrupt Message Store
A scalable interrupt mechanism for the cloud
MEGHA DEY
Linux Kernel Engineer

## Slide 2
AGENDA
Evolution of I/O virtualization
Scalable I/O Virtualization (SIOV) architecture
The interrupt story so far
Need for Interrupt Message Store
Interrupt Message Store advantages
Linux* IRQ subsystem
Hierarchical domains
Linux IMS design
IMS example use case
Current status
Summary

## Slide 3
Evolution of I/O Virtualization
@twitter handle
Device emulation
Para virtualization
Single root I/O virtualization (SR-IOV)
Scalable I/O virtualization (SIOV)
Software techniques
Hardware assisted
Direct device assignment

## Slide 4
Evolution of I/O Virtualization
@twitter handle
Para virtual I/O
Device emulation
Performance
Scalability
SR-IOV
SIOV
Direct device assign
Device emulation
Para virtualization
Direct device assignment
SR-IOV
SIOV
Scalability: Sharing of I/O devices across different VMs
Performance: How fast guest OS can access device

## Slide 5
SIOV Architecture
@twitter handle
VDCM: Virtual Device Composition Module ADI: Assignable Device Interface BR: Backend Resources
BR 1
BR 2
BR 4
BR 3
BR K
FAST PATH
…..………
……………
…………
AN SIOV DEVICE
HOST VMM S/W
SLOW PATH
SLOW PATH
FAST PATH
FAST PATH
FAST PATH
SLOW PATH
VDCM
VDCM
VDCM
GUEST 1
GUEST 2
GUEST n
VIRTUAL DEVICE 1
VIRTUAL DEVICE n
VIRTUAL DEVICE 2
ADI 1
ADI 2
ADI 3
ADI m
Each ADI may use multiple interrupts

## Slide 6
SIOV Devices
@twitter handle
INTERRUPT MESSAGE STORE (IMS)
Is there a matching interrupt mechanism?
High-performance devices
GPU devices
RDMA capable devices
Data accelerators
NVM Express* storage controllers
High bandwidth network controller devices
Reconfigurable FPGA devices

## Slide 7
The Interrupt Story… So Far
@twitter handle
MSI: Message Signaled Interrupt
  Pin based
  Wired
  Shared
  Reduced performance
Legacy interrupts
  Memory write
  Stored as address/data pairs
  Never shared
  Max 32 messages
MSI
  Extension to MSI
  Stored in MSI-X table
  Individually configurable
  Max of 2048 vecs
MSI-X
Is 2048 enough?

## Slide 8
Need for IMS
@twitter handle
BR 1
BR 2
BR 4
BR 3
BR K
FAST PATH
…..………
……………
…………
AN SIOV DEVICE
HOST VMM S/W
SLOW PATH
SLOW PATH
FAST PATH
FAST PATH
FAST PATH
SLOW PATH
VDCM
VDCM
VDCM
GUEST 1
GUEST 2
GUEST n
VIRTUAL DEVICE 1
VIRTUAL DEVICE n
VIRTUAL DEVICE 2
ADI 1
ADI 2
ADI 3
ADI m
n = 1000
m = 2
k = 2
Total interrupt messages required = n * m * k = 1000 * 2 * 2 = 4000 (>> 2048)

## Slide 9
Interrupt Message Store
@twitter handle
Device specific
Access through host driver
No limit on size
On-device
or system memory
Unified or multiple
Follows MSI-X format
Device can support both IMS and MSI-X
Uses remappable format

## Slide 10
IMS advantages
@twitter handle
Scalable
Reduced OS enabling
Flexible
Dynamic
Device specific
Access through host driver
No limit on size
On-device or system memory
Unified or multiple

## Slide 11
@twitter handle
Linux* Interrupt Subsystem
1. IRQ chip
2. IRQ domain
3. IRQ desc
4. IRQ data
Controller local HWIRQs
Global unique Linux IRQ number

## Slide 12
Hierarchical Domains
@twitter handle
DMAR-MSI
INTEL IR
APIC
Interrupt delivery path in a modern X86 system
IRQ CHIP
IO IR APIC
IO APIC IR 0
IR PCI MSI
Intel IR MSI
IRQ domain
Device A
Device B
Device C
Intel IR 0
DMAR-MSI
Vector
Intel IR 1

## Slide 13
Linux* IMS Design
@twitter handle
IRQ core: (arch/x86/kernel/apic/)
Create IMS chip, IMS domain
IRQ remapping: (drivers/iommu/)
Support IMS domain
X86 core: (arch/x86)
Setup/teardown mechanisms
Drivers core: (drivers/base)
Allocate and free IRQs, IRQ chip callbacks
dev_ims_alloc_irqs
dev_ims_free_irqs

## Slide 14
Where does IMS fit in?
@twitter handle
DMAR-MSI
INTEL IR
APIC
Interrupt delivery path in a modern X86 system
IRQ CHIP
IO IR APIC
IO APIC IR 0
IR PCI MSI
Intel IR MSI
IRQ domain
Device A
Device B
Device C
Intel IR 0
DMAR-MSI
Vector
Intel IR 1
IR DEV-IMS
Intel Dev IMS
Device D

## Slide 15
Driver Changes to Support IMS
@twitter handle
Device specific callbacks:
mask, unmask, write_msg
Driver must specify:
Size of device IMS
Location of device IMS

## Slide 16
IMS Example Usage
@twitter handle
1. Load the native device driver
2. Load the vfio-mdev module
3. Create mediated device
4. Pass mdev to *guest (e.g., *qemu)
5. Run some device operation in guest
6. Check /proc/interrupts:
in host: IMS interrupts
on guest: either IMS or MSI-X
On host:
On guest:

## Slide 17
Current Status
@twitter handle
IMS infrastructure patches ready, testing done on simulator
To be sent to Linux* Kernel Mailing List (LKML) for review
Group based IMS allocation:
Submitted RFC patch for dynamic MSI-x:
https://lkml.org/lkml/2019/6/21/923

## Slide 18
Summary
@twitter handle
IMS is a scalable interrupt mechanism for SIOV devices
Its size and location are device specific
A new IMS IRQ chip and IRQ domain has been added support IMS interrupts
IMS spec: https://software.intel.com/sites/default/files/managed/cc/0e/intel-scalable-io-virtualization-technical-specification.pdf
  Section 3.4.1

## Slide 19
Thank you!
Questions?