## Slide 1: PASID/IOASID Management in Linux Linux Plumbers 2019 VFIO/IOMMU/PCI Track Yi Liu <yi.l.liu@intel.com>, Jacob Pan <jacob.jun.pan@linux.intel.com>

## Slide 2: PASID/IOASID lifecycle
Allocation/free
  IOASID allocator, emulated guest allocator
  Mapping (Identical mapping: System wide PASID namespace gPASID=hPASID or Non-identical gPASID != hPASID)
Bind/unbind PASID to process mm
Exceptions
  Guest process termination, VM crash (FD close, Clear pending faults)
  Host process termination - mmu_notifier release
  IOMMU device fault reporting
  Device abort PASID

## Slide 3: vSVA Upstream Plan
PCI device no page fault*
Page request service
Mediated device
(un)bind_gpasid() /* Intel */ cache_invalidate() Ioasid_alloc/free/set_data() | register_dev_fault_handler() report_device_fault Start/Stop_pasid() /* address race with device PASID abort, pending fault */ Iommu_page_response() | Set_fault_handler_data() /* multiple data (per PASID) per handler */ Virtual device composition module
IOMMU APIs and related VT-d patches
*Current patchset posted on v5 https://lkml.org/lkml/2019/8/15/951
Notes: PRQ support for multiple mdev

## Slide 4: vSVA work flow
Dev
Host
VMM
devices
devices
Physical
device
VFIO/
IOMMU
Guest
kernel
Work
Submission, device control
DMA
vIOMMU
Assigned
device
Assigned
device
Bind_mm
Alloc PASID
Bind_gpasid
Flush PASID
App
IOMMU
device
PASID programming
Faults
(Page request service (PRS)
unrecoverable faults)
Page
response
Page request
Page request
Page
response
Race conditions during PASID termination
Setup (slow path)
Work (fast path)

## Slide 5: Issues
PASID level abort may take a long time, cannot use FLR, unregistration of fault handler cannot fail
  Proposal: iommu_stop/start_pasid()
  Usage: pasid_stop() ---- pasid abort () --- unregister_fault_handler ---- pasid_unbind
To support page request on mdev, fault reporting at PASID level
  Proposal: Add multiple handler data support, per device handler, per PASID data
  Usage:
    iommu_register_device_fault(dev, handler, data)
    Iommu_add_device_fault_data(dev, pasid, hdata)
    Iommu_report_device_fault(dev, evt, data)
Misbehaving guests w.r.t page request/response
  Timer based, send IR response code after timeout
  Quota based, each guest can have so many outstand PR
Notes: iommu_stop/start_pasid(): mark PASID not present, clear pending faults, flush iotbl, flush device tlb, auto response page requests with code IR afterwards.
Inject UR to guest if illegal pasid is used.

## Slide 6
IOMMU driver
IOASID allocator
VCMD_REG
Guest
ALLOC_PASID
IOMMU driver
IOMMU
Hypervisor
HW
Host
vIOMMU
Request hPASID
Device Driver
VM PASID Manager
IOASID
Allocator
g/h PASID?
gPASID
Allocator
g/h map
VM PASID Manager Architecture
Application
Device
IOASID tracking
IOASID
Allocator
Program PASID
Virtual Device
Composition Module
Default IOASID
SVA IOASID